## Slide 1
Debug Interface
CubeSat C3 Unit
USB Power
Data inout
CubeSat C3 Unit Level 0
Module | CubeSat C3 Unit
Bi-directional (Input-Output) | USB Power : supplies 4.5V-5.5V to the board and feeds data into and out of the system Debug Interface : Debug with JTAG interface Peripherals: Connection via GPIO to other components, for e.g. LEDs, audio-channel etc. RFIO: Radio input-output channel at 436.5 MHz passband ; uses an antenna
Functionality | This module is a subsystem of a larger satellite CubeSat system. The main function of this subsystem is to receive and transmit high frequency data signal using Wi-Fi protocol. At the heart of this module is a microcontroller that takes commands via USB, GPIO, and JTAG configurations and uses radio frequency to communicate messages from and to another similar module.
Antenna

## Slide 2
CubeSat C3 Unit Level 1
Debug Interface
Antenna
USB/UART Power
Data inout
Power Manage-
ment
MCU
USB2UART
LEDS
RF Front End
GPIO
JTAG

## Slide 3
Module | Power Management
Input | USB Power : supplies 4.5V-5.5V DC through USB connection
Output | Vout: Outputs 3.3 V DC
Functionality | The function of this unit is to manage the power system. It is powered through USB connection. It consists of voltage regulator and a battery pack that stores voltage and outputs constant 3.3V.
Module | USB2UART
Bidirectional (Input –Output) Output | USB : Data via USB connection (D+ and D-) UART: Data via UART (RX and TX)
Functionality | This unit consists of USB-to-UART Bridge controller that converts USB signals to RS-232 and vice-versa.
Power
Management
Vout
3.3V
USB Power
USB2UART
UART
USB
Level 1 Breakdown

## Slide 4
Module | GPIO
Input | Vin: 3.3 V DC
Bi-directional (input-output) | Data: common channel for data in and out using GPIO connection
Functionality | This modules provides an interface between microcontroller units other peripherals.
Module | JTAG
Input | Vin: 3.3 V DC
Bi-directional (input-output) | Debug signals: Common channel to transfer data between microcontroller and environment.
Functionality | This consists of a 10-pin JTAG connector system that allows to debug the chip.
GPIO
Data
Vin
3.3 V
JTAG
Debug
signals
Vin
3.3 V
Level 1 Breakdown

## Slide 5
Module | LEDs
Input | Vin: 3.3 V voltage supply GPIO: GPIO pins connection
Functionality | There are total 7 LEDs: 1 single and 3 tri-colored LEDs indicate battery connection; 3 other tri-colored LEDs are used as Status indicator of connection of JTAG, and receive and transmit of RF signals.
Module | RF Front End
Input | Vin: 3.3 V supply
Bidirectional (Input –Output) | RFIO: 0-13dB power signals at 436.5 MHz
Antenna | It is used for both to transmit and receive signals
Functionality | The main purpose of this module is to receive and transfer radio signals at a passband frequency of 436.5 Hz.
LEDs
GPIO
Vin
RF Front End
RFIO
436.5 MHz
Vin
3.3 V
Level 1 Breakdown
Antenna

## Slide 6
Level 1 Breakdown
Module | MCU
Input | Vin: supplies 4.5V-5.5V
Output | LEDs : Tri-colored LEDs (RGB)
Bi-directional (Input-Output) | GPIO: Connection to peripherals via GPIO JTAG: connection to 10-pin JTAG interface RFIO: Radio input-output channel at 436.5 MHz passband
Functionality | This is the main microcontroller unit in the system. It uses a real-time operating system.It has a resonator connected to it that clocks at 32MHz. This unit monitors radio signals, as well as provides multiple interfaces , for eg.GPIO, JTAG, SPI, I2C etc., to transmit and receive data.
JTAG
RFIO
MCU
Vin (3.3V)
GPIO
LEDs

## Slide 7
UML Activity View of CubeSat C3 Unit

## Slide 8
UML Sequence Diagram View of CubeSat C3 Unit
CubeSat C3
Unit 2
Transmit Packet
(via Antenna)
User 2
Confirmation Packet
(via Antenna)
User 1
CubeSat C3
Unit1
Event Trigger
(SPI protocol)
Solid Status LEDs
(Transmit Failed)
Blink Status LEDs(
Transmit Success)
Blink Status
LEDS twice
(Packet Received)