## Slide 1
!Reset
CubeSat C3 Unit
Power
On/Off
CubeSat C3 Unit Level 0
Antenna
Debug
Peripherals
Module | Power Management
Input | Power: USB or Battery On/Off: Enables and Disables the Voltage Regulator !Reset: Reset Button
Bi-Directional (Input-Output) | Antenna: Radio Antenna with 436.5MHz passband Peripherals: At discretion of user, breakout pins Debug: Debug with JTAG
Functionality | This module is a subsystem of a larger satellite CubeSat system. The main function of this subsystem is to receive and transmit high frequency data signal using Wi-Fi protocol. At the heart of this module is a microcontroller that takes commands via USB, GPIO, and JTAG configurations and uses radio frequency to communicate messages from and to another similar module.

## Slide 2
CubeSat C3 Unit Level 1
Peripherals
Antenna
USB
!Reset
Power Manage-
ment System
MCU
USB2UART
RF Filter
Battery
Debug

## Slide 3
Module | Power Management
Input | USB Power : 4.5~5.5V DC
Output | Vout: Outputs 3.3 V DC
Bidirectional (Input –Output) | Battery: 3.9V 1000mAH
Functionality | The function of this unit is to manage the power system. It is powered through USB connection. It consists of voltage regulator and a battery pack that stores voltage and outputs constant 3.3V.
Module | USB2UART
Bidirectional (Input –Output) | USB : USB connection (D+ and D- lines) UART0: RX and TX lines to MCU UART0 pin
Functionality | This unit consists of USB-to-UART Bridge controller that converts USB signals to RS-232 and vice-versa.
Power
Management
Vout
3.3V
USB Power
USB2UART
UART0
USB
Level 1 Breakdown
Battery

## Slide 4
RF Front End
RFIO
436.5 MHz
Level 1 Breakdown
Antenna
Module | RF Filter
Bidirectional (Input –Output) Output | RFIO: 0-13dB power signals at 436.5 MHz Antenna: Signal goes through antenna
Functionality | The main purpose of this module is to receive and transfer radio signals at a passband frequency of 436.5 Hz.

## Slide 5
Level 1 Breakdown
Module | MCU
Input | Power Management System !Reset: Reset button
Bi-directional (Input-Output) | Peripherals: Connection to peripherals which are at users discretion Debug: Connection to 10-pin JTAG interface RFIO: Radio input-output channel at 436.5 MHz passband UART0: Rx and Tx lines for UART0 port on MCU
Functionality | This is the main microcontroller unit in the system. It uses a real-time operating system.It has a resonator connected to it that clocks at 32MHz. This unit monitors radio signals, as well as provides multiple interfaces , for eg.GPIO, JTAG, SPI, I2C etc., to transmit and receive data.
Debug
RFIO
MCU
!Reset
UART0
Peripherals
Power Management System

## Slide 6
UML Activity View of CubeSat C3 Unit

## Slide 7
UML Sequence Diagram View of CubeSat C3 Unit
CubeSat C3
Unit 2
Transmit Packet
(via Antenna)
User 2
Confirmation Packet
(via Antenna)
User 1
CubeSat C3
Unit1
Event Trigger
(SPI protocol)
Solid Status LEDs
(Transmit Failed)
Blink Status LEDs(
Transmit Success)
Blink Status
LEDS twice
(Packet Received)