## Slide 1: CubeSat C3 Board (Command, Control and Communication)
Team: T05
William Harrington
James Heath
Shan Quinney
Michael Mathis
Saroj Bardewa

## Slide 2: Need
PSAS’s mission is to get a CubeSat into Lower Earth Orbit
Need for a device for command, control and communication (C3) between a CubeSat and a ground station
Board with specific functionalities and broadcast Frequency (436.5 MHz)
Notes: Problem or Need : What is the problem being solved? Where does it arise?
 Portland State Aerospace Society has a need of a device that can communication between a CubeSat and a ground Station. The commercial Boards
2

## Slide 3: Motivation
Take a small part in PSAS’s CubeSat Mission
Notes: Motivation: Why is it important? What is the value of a solution?
Andrew solicited the class to build a system with his specifications
3

## Slide 4: Objective
Build a working prototype to meet the requirements
Notes: What is the specific objective of this project?A design? Aworking prototype?
4

## Slide 5: Requirements
Must:
Be a breakout board
Have a transceiver for RF communications
Have a visible indication of communication
Have an antenna capable of 435-438 MHz frequency band transmission
Able to fit within CubeSat form factor (no bigger than (10cm x 10cm x 10cm)
Have access to UART, I2C,SPI,GPIO and ADCs/DACs

## Slide 6: Requirements (Cont.)
Should:
Use USB interfacing
Be able to send/receive data packets via RF communication
Be battery powered
If battery powered, utilize USB for recharging
May:
Be capable of long distance communication
Be capable of sending/receiving data packets
Be capable of operation in space temperature range (-30C to 60C)

## Slide 7: Alternative
Freescale MRB-KW019032NA
Notes: What other alternatives exists?
 MRB-KW0x board, but it does not meet the frequency needs and other limitations
7

## Slide 8: Approach
The approach was to make a breakout board that was easy to interface and test and capable of RF communication.
User-centered design

## Slide 9: Design - Level 0
Notes: May need multiple subAheadings here (e.g. H/W and S/W, or multiple subsystems) Describe design using appropriate methods (e.g. UML models, algorithms) Discuss design alternatives, tradeAoffs, decisions made
9

## Slide 10: Design - Level 1
Notes: May need multiple subAheadings here (e.g. H/W and S/W, or multiple subsystems) Describe design using appropriate methods (e.g. UML models, algorithms) Discuss design alternatives, tradeAoffs, decisions made
10

## Slide 11: Implementation - Tools
Eagle CAD for PCB layout
OpenOCD for debugging
Multimeter
JTAG connector
Oscilloscope
USB to micro-USB cable
VNA
Notes: Tools employed (e.g. simulation/modeling tool, PCB layout, IDE, crossAcompilers)
11

## Slide 12: Implementation: Code
SPI Configuration
Communication with Transceiver
Functional GPIO
Clock Routing
Toolchain

## Slide 13: Implementation - Schematics
Notes: 13

## Slide 14: USB to UART

## Slide 15: Battery Charger

## Slide 16: Voltage Regulator

## Slide 17: RF Filter

## Slide 18: JTAG and Reset

## Slide 19: MCU

## Slide 20: Board Layout
Notes: 20

## Slide 21: Finished Board
Notes: 21

## Slide 22: IP and Prior Work
Helpful resources:
MKW01Z128 : Highly-integrated, Cost-effective Single-package Solution for Sub 1 GHz Applications
MKW01xxRM: Sub 1 GHz Low Power Transceiver plus Microcontroller Reference Manual
KW01 Development Hardware: Reference Manual
All open source
Notes: Brief summarize what use you made of prior work or IP including but not limited to ideas, designs, schematics, board layouts, code.
22

## Slide 23: Testing
Prodded test points with OSC/MM to check voltage over the board (3.3V, Vbus, clock, etc.)
Rapidly prototyped filter boards and tested with the VNA
Self-checking via LEDs
Notes: Example of System Testing
23

## Slide 24: Testing (Cont.)
Test Matrix goes here
Notes: Example of Interface Testing
24

## Slide 25: RF Results
We were not able to implement the radio due to time restraints on firmware coding
RF Filter worked as tested by the prototype boards
Antenna testing with the protoboards also showed a success on the VNA

## Slide 26: Firmware Results
Notes: Results What worked? How well? What didn’t? Why?
26

## Slide 27: Firmware Results (Cont.)

## Slide 28: Firmware Results (Cont.)

## Slide 29: Contributions
RF (Team Black Magic AF)
  Shan
  Jake
Firmware (Team Bare Metal AF)
  Will
  Mike
Video/Documentation
  Saroj
Notes: What were the contributions of each member (e.g. who did PCB, coding, testing, writing)?
29

## Slide 30: Lessons Learned
Overly Ambitious
  Weren’t prepared for difficulty
Start Programming Earlier
Team Accountability

## Slide 31: Acknowledgments
Portland State University
Aerospace Society (PSAS)
Theo Hill of PSAS
Devin ECE411 TA
Notes: 31